## Slide 1
Beyond clever presentation:
Volkswagen’s emissions test
Team 5 · When did a company seriously manipulate its data?
What did VW do to the test? What was it trying to achieve? Who paid the price?
Notes: Planned time: 60 seconds. Volkswagen sold diesel cars in the United States as clean and compliant. Our question is when that stopped being flattering presentation and became manipulation of the data itself. We will answer three questions: what Volkswagen did to the test, what it was trying to achieve, and who paid the price. Along the way we will show exactly what was measured, how a correct laboratory number became misleading, and how independent road testing exposed it. Our central source is a 2014 university report. The EPA’s 2015 notice and Volkswagen’s 2017 admitted statement of facts answer questions that this small study could not. I will keep those sources separate, so that no number carries more meaning than its evidence supports. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014; EPA, Notice of Violation CAA-09-18-15, 18 September 2015; United States v. Volkswagen AG, Plea Agreement, 11 January 2017, Exhibit 2 (Statement of Facts), ¶ 30. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 2
The claim and the measurement
The claim
Compliance with U.S. standards
Vehicles marketed as clean diesel
Certification supported market access
The quantity
NOx mass per distance
Nitrogen oxides in the exhaust
Measured in grams per kilometre
Reference standard: 0.043 g/km NOx at full useful life
WVU/ICCT (2014), Table 2.2 p. 5 (0.07 g/mi), Table 4.1 p. 59 (0.043 g/km); VW plea (2017), Exh. 2, ¶¶ 28–30, 32 (Exh. 2 pp. 10–12).
2
Notes: Planned time: 70 seconds. NOx means nitrogen oxides, a group of air pollutants produced during combustion. Grams per kilometre is a mass-per-distance unit: it tells us how much NOx leaves the exhaust for each kilometre travelled. The benchmark in the original report is the U.S. Tier 2 Bin 5 NOx standard, 0.043 grams per kilometre at full useful life. Full useful life is the regulatory durability period. It does not mean the researchers followed each car for its entire lifetime. The later admitted facts describe clean-diesel marketing and a strategy to sell vehicles in the U.S. The measurement mattered because buyers and regulators needed to know whether the claimed emissions performance held beyond the conditions used to obtain approval. The study therefore asked a practical question: what did these vehicles emit when researchers took the instruments onto the road? SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, Table 2.2 p. 5 (0.07 g/mi), Table 4.1 p. 59 (0.043 g/km); United States v. Volkswagen AG, Plea Agreement, 11 January 2017, Exhibit 2 (Statement of Facts), ¶¶ 28–30, 32 (Exh. 2 pp. 10–12). WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 3
Laboratory and road measurements
Laboratory
Prescribed conditions
A chassis dynamometer simulates driving
FTP-75 uses a standard speed sequence
Road
Changing conditions
PEMS measures exhaust on a moving car
Traffic, gradient and load vary
The standard is a reference for road results; road routes are not certification cycles.
WVU/ICCT (2014), pp. 9, 39–55, 59, 64.
3
Notes: Planned time: 75 seconds. A chassis dynamometer is a set of rollers that lets a car run through a driving sequence while staying inside a laboratory. FTP-75 is the standardised U.S. driving sequence used for the laboratory averages shown later. The road measurement used PEMS, a portable emissions measurement system. The equipment travelled with the car and measured exhaust gases and flow, alongside information about the journey. Combining pollutant mass with distance gives grams per kilometre. Road conditions vary. An uphill stretch can increase engine load. Traffic changes acceleration and stopping. Those differences are legitimate reasons to expect some variation between laboratory and road measurements. A gap therefore needs explanation, rather than an immediate accusation. There are two comparisons to keep separate. Comparing a road average with 0.043 asks how it relates to the standard. Comparing it with that same vehicle’s laboratory average asks how much the measured behaviour changed between conditions. The denominators differ, so the ratios differ too. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, pp. 9, 39–55, 59, 64. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 4
Three vehicles, with limited coverage
Vehicle A
2.0 L
Lean-NOx trap
Vehicle B
2.0 L
Urea-SCR
Vehicle C
3.0 L
Urea-SCR
Road tests: A, B, C Laboratory tests: A, B
Three case studies do not estimate fleet-wide prevalence.
WVU/ICCT (2014), p. iv; pp. 1, 9–10; Table 3.15 p. 57. EPA NOV (2015), p. 4 (2012 Jetta, 2013 Passat).
4
Notes: Planned time: 75 seconds. West Virginia University performed the study for the International Council on Clean Transportation; the final report is dated May 15, 2014. The report anonymised the cars as A, B and C. The EPA later identified the two high emitters as a 2012 Volkswagen Jetta and a 2013 Volkswagen Passat, but not which letter is which, so I keep the report’s labels. Vehicle A used a lean-NOx trap, which stores nitrogen oxides and periodically treats them. B and C used urea-based selective catalytic reduction, or SCR, which uses a reagent and a catalyst. All three were road-tested; only A and B were also tested in the laboratory. The five California routes covered highway, city and rural hill driving, with some vehicle-route combinations missing. These are three individual vehicles, not a random sample. The report explicitly restricts its conclusions to them. Repeated runs help assess consistency within these cases; they do not turn three cars into a fleet estimate. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, p. iv; pp. 1, 9–10; Table 3.15 p. 57. EPA, Notice of Violation CAA-09-18-15, 18 September 2015, p. 4 (2012 Jetta, 2013 Passat). WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 5
The measured NOx results
Chart: Mean NOx (g/km)
| Study lab FTP-75 | R1 Highway | R2 Los Angeles | R3 Rural hills | R4 San Diego | R5 San Francisco
Vehicle A (lean-NOx trap) | 0.022 | 0.614 | 0.989 | 1.505 | 1.48
Vehicle B (urea-SCR) | 0.016 | 0.344 | 0.809 | 0.671 | 0.675 | 0.815
Vehicle C (urea-SCR) | 0.048 | 0.07 | 0.409 | 0.053
Tier 2 Bin 5 standard, 0.043 g/km | 0.043 | 0.043 | 0.043 | 0.043 | 0.043 | 0.043
Bars: route or test means; thin bars: ±1 SD as published (none for single runs). No bar = no test (C lab, C R4, A R5), not zero.
The standard is a certification benchmark, used here as a reference; road routes are not certification tests. Three vehicles: no fleet-wide estimate.
WVU/ICCT (2014), Table 4.3 p. 65; p. 64; Table 4.1 p. 59.
5
Notes: Planned time: 95 seconds. Here is the evidence chart, using the original report’s numbers. The vertical axis is linear and starts at zero. The colours identify Vehicles A, B and C. The red dashed line is 0.043 grams per kilometre, the reference standard. The left group contains laboratory FTP-75 averages: 0.022 for A and 0.016 for B. There is no laboratory result for C. The remaining groups are the five road routes. An absent bar means no result for that vehicle and route. Vehicle A’s highway mean is 0.614. Its rural hill mean rises to 1.505, and its San Diego mean is 1.480. B ranges from 0.344 to 0.815 across these five routes. C’s means are much lower on most routes, but its rural hill mean reaches 0.409. Each bar is an average, not a peak. For example, Vehicle A’s two San Diego runs were 1.24 and 1.72 grams per kilometre; the bar shows their mean, 1.480. The thin error bars are the standard deviations the researchers published. Single runs have no reported deviation. The pattern is large, vehicle-specific and sensitive to route conditions. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, Table 4.3 p. 65; p. 64; Table 4.1 p. 59. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 6
The denominator changes the meaning
35.0×
1.505 ÷ 0.043
Vehicle A, rural road mean
relative to the standard
≈68×
1.505 ÷ 0.022
The same road mean relative to
A’s lab mean (0.022 ± 0.006, two tests)
Report summary: A ≈15–35×; B ≈5–20× the standard, depending on route
WVU/ICCT (2014), pp. ii–iii (cold start), 62–65; p. 64 (single runs). VW plea (2017), Exh. 2, ¶ 52 (Exh. 2-21). Ratios are our calculations from published means.
6
Notes: Planned time: 90 seconds. Let us work through one number. For Vehicle A on the rural hill route, 1.505 divided by 0.043 is 35.0: the road mean relative to the standard. Divide the same 1.505 by A’s own laboratory average of 0.022 and you get about 68: a road-to-laboratory ratio. Same measurement, different denominator, different headline. That laboratory average comes from only two tests, 0.022 plus or minus 0.006, so treat 68 as an order of magnitude. The laboratory figure also includes a cold start, while the road runs were warm; the report notes that cold starts usually raise NOx, so this does not inflate the road side. The report summarises A at about 15 to 35 times the standard and B at about 5 to 20 times. In this five-route table the means give A 14 to 35 and B 8 to 19. Later documents use other figures: the plea agreement says up to about 40 times for the study vehicles, which matches A’s single highest run, 1.72 divided by 0.043. Always ask which number, divided by what. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, pp. ii–iii (cold start), 62–65; p. 64 (single runs). Plea Agreement, Exhibit 2, ¶ 52 (Exh. 2-21). Ratios are our calculations from published means. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 7
An anomaly still needs testing
Measurement
Check calibration and method agreement
Operating conditions
Check route, temperature, load and regeneration
Inference
Separate a measured gap from its cause
WVU/ICCT (2014), §3.3.3.3 p. 50 and Table 3.13 p. 55; Table 3.15 p. 57; pp. 62–64; Table 4.3 p. 65; p. iv.
7
Notes: Planned time: 65 seconds. Before blaming software, a skeptical analyst asks whether the measurement itself could explain the gap. The researchers checked the portable equipment against laboratory equipment on Vehicle B. The agreement was not perfect: Table 3.13 shows an 18.8 percent NOx difference on the weighted FTP-75. But an 18.8 percent method difference cannot produce a 15- or 35-fold gap. It is a scale comparison, not a correction factor. The researchers also considered operating explanations: diesel-filter regeneration, the periodic burning-off of trapped soot, as well as control strategy, catalyst sizing and urea dosing. Road load and traffic matter too. Finally, the dataset is small: missing vehicle-route combinations, few repeats, and a repeat-count inconsistency for C’s rural route between the report’s test matrix and its results table. The right conclusion is a serious anomaly that demands follow-up, not a fleet-wide estimate and not yet proof of intent. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, §3.3.3.3 p. 50 and Table 3.13 p. 55; Table 3.15 p. 57; pp. 62–64; Table 4.3 p. 65; p. iv. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 8
What VW did to the test
The “switch” read steering position, speed, engine run time and barometric pressure
Official test recognised
“Dyno calibration”
Full emissions control:
compliant laboratory results
Normal driving
“Road calibration”
SCR / lean-NOx-trap control
weakened on the road
Summary of EPA NOV pp. 3–4 and plea ¶¶ 34, 49–50; a simplification, not the source code
EPA NOV (2015), pp. 3–4; VW plea (2017), Exh. 2, ¶ 34 (Exh. 2 pp. 12–13), ¶¶ 49–51 (Exh. 2 pp. 19–20).
8
Notes: Planned time: 75 seconds. So what exactly did Volkswagen do to the test? The later investigation supplied the mechanism that the road study could not. According to the EPA notice, software in the engine computer, which the EPA called the “switch”, read inputs such as steering-wheel position, vehicle speed, how long the engine had been running and barometric pressure. Those inputs track the official U.S. test procedure. When the switch recognised the test, the car ran a “dyno calibration” with full emissions control. The rest of the time it ran a “road calibration” that reduced the effectiveness of its exhaust treatment. Volkswagen’s admitted facts say the software recognised the published drive cycles, and that in 2013 a supervisor approved adding steering-angle recognition, because a car on test rollers does not steer. So Volkswagen did not falsify a spreadsheet. It made the measured object change its behaviour when measured. The laboratory reading could be accurate and still misrepresent ordinary driving. SOURCE (not spoken): EPA, Notice of Violation CAA-09-18-15, 18 September 2015, pp. 3–4; United States v. Volkswagen AG, Plea Agreement, 11 January 2017, Exhibit 2 (Statement of Facts), ¶ 34 (Exh. 2 pp. 12–13), ¶¶ 49–51 (Exh. 2 pp. 19–20). WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 9
Where the line was crossed
LINE CROSSED
2006
Design decision
Engine could not meet NOx rules and still sell; software built to detect the test
¶¶ 33–36
2009–15
Sales
About 585,000 U.S. vehicles sold with defeat software
¶ 72
2013
Refinement
Steering-angle recognition approved to spot the test
¶¶ 49–50
2014
Independent data
WVU road tests expose the gap; regulators ask why
¶¶ 52–53; EPA p. 4
2014–15
Concealment
False explanations; recall with only limited benefit
¶¶ 54–58; EPA p. 4
Sept 2015
Admission
Defeat device admitted on 3 Sept; EPA notice on 18 Sept
¶¶ 63–64
The line: engineering the product so the official measurement would not represent normal use, then hiding it
VW plea (2017), Exh. 2, ¶¶ 33–36 (Exh. 2 pp. 12–14), 49–58 (pp. 19–23), 59, 63–64 (pp. 23–25), 72 (p. 27). EPA NOV (2015), pp. 1, 4.
9
Notes: Planned time: 85 seconds. Where exactly was the line crossed? Not in 2014, when the numbers looked bad, and not in how anyone drew a chart. According to Volkswagen’s admitted facts, around 2006 engineers concluded they could not build a diesel engine that met the stricter U.S. NOx standards and still attracted enough customers. Instead of changing the engine, they built software to detect and defeat the test. When staff objected, a senior supervisor decided to continue and told them, in substance, not to get caught. That is the line: deliberately engineering the product so that the official measurement would not represent normal use. From 2009, about 585,000 U.S. vehicles were sold with defeat software. In 2013 it was refined with steering-angle recognition. After the 2014 study, Volkswagen gave regulators false explanations, such as driving patterns and technical issues, and a recall that the EPA says brought only limited benefit. On 3 September 2015, with its 2016 models awaiting certification, Volkswagen admitted the defeat device. The EPA notice followed on 18 September. Every step after 2006 was concealment of a decision already made. SOURCE (not spoken): United States v. Volkswagen AG, Plea Agreement, 11 January 2017, Exhibit 2 (Statement of Facts), ¶¶ 33–36 (Exh. 2 pp. 12–14), 49–58 (pp. 19–23), 59, 63–64 (pp. 23–25), 72 (p. 27). EPA, Notice of Violation CAA-09-18-15, 18 September 2015, pp. 1, 4. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 10
What VW wanted, and who paid
What VW wanted
U.S. diesel sales: pass the NOx standard on paper and still attract buyers; later, keep approval for 2016 models
Volkswagen AG
Guilty plea to three felonies: $2.8 billion criminal fine + $1.5 billion civil penalties; 3 years’ probation with an independent monitor
Owners and the public
≈585,000 U.S. vehicles; owner settlements and a NOx remediation trust credited at $11 billion; extra NOx exposure not quantified in our sources
VW plea (2017): offences p. 1; monitor p. 12; civil penalties, $11B credit and $2.8B fine p. 13; probation p. 14. Exh. 2 ¶¶ 30–33 (Exh. 2 pp. 10–12), 54–55, 59, 61, 72 (p. 27).
10
Notes: Planned time: 75 seconds. What was Volkswagen trying to achieve? Its admitted facts give the motive. Selling diesel cars in the United States was an important strategic goal, and engineers could not meet the stricter NOx standards while still attracting enough customers. The software let the cars pass certification without that trade-off. Later, concealment aimed to keep approval for the 2016 models. Who paid the price? Volkswagen AG pleaded guilty to three felonies: a criminal fine of 2.8 billion dollars and 1.5 billion dollars in civil penalties, plus three years of probation under an independent monitor. The plea also credits 11 billion dollars already committed to owner settlements and a NOx remediation trust. Owners bought about 585,000 cars marketed as clean diesel that did not meet the standard they were sold on. People near those cars were exposed to extra NOx; none of our sources quantify that health cost, so I will not put a number on it. And regulators spent more than a year receiving false explanations. SOURCE (not spoken): United States v. Volkswagen AG, Plea Agreement, 11 January 2017: offences p. 1; monitor p. 12; civil penalties, $11B credit and $2.8B fine p. 13; probation p. 14. Exhibit 2 (Statement of Facts) ¶¶ 30–33 (Exh. 2 pp. 10–12), 54–55, 59, 61, 72 (p. 27). WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 11
Why this crossed into manipulation
Selective presentation
Choosing favourable observations while leaving other observations out
Documented manipulation
Changing behaviour when the test is recognised and concealing that change from decision-makers
Analytical interpretation grounded in VW plea (2017), Exh. 2 ¶¶ 33–35, 54–55, 63; EPA NOV (2015), p. 4.
11
Notes: Planned time: 65 seconds. Selective presentation means choosing favourable observations and omitting less favourable ones. It can mislead even when the individual numbers are correct. The documented Volkswagen conduct went further: the vehicle’s behaviour changed when the software recognised the test, and that mechanism was concealed. The certification result could be an accurate reading of exhaust under the tested settings. The deception lay in making that conditional result stand for a vehicle whose emissions controls operated differently during ordinary use, while withholding the reason. The broader analytics lesson is to distinguish data accuracy from the validity of the conclusion drawn from it. A number can be accurate, yet the process that generates it can make the intended comparison misleading. Independent testing helped expose that weakness, and the later investigation established why it existed. SOURCE (not spoken): Analytical interpretation grounded in United States v. Volkswagen AG, Plea Agreement, 11 January 2017, Exhibit 2 (Statement of Facts), Exh. 2 ¶¶ 33–35, 54–55, 63; EPA, Notice of Violation CAA-09-18-15, 18 September 2015, p. 4. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 12
What a skeptical analyst should check
1
Meaning
Unit, averaging method and denominator
2
Coverage
Routes, missing tests and repeat counts
3
Independence
Instrument checks and tests outside the standard cycle
4
Causation
Alternative explanations, software evidence and admissions
Analytical recommendations based on WVU/ICCT (2014), pp. iv, 55, 57, 59, 64–65, and VW plea (2017), Exh. 2 ¶¶ 33–35, 54–55, 63.
12
Notes: Planned time: 75 seconds. A skeptical analyst would start with the meaning of the number. Is it grams per kilometre, a peak, an average, or a ratio? What is the denominator? Our example changed from 35 to 68 simply by changing the comparison. Next comes coverage. Which vehicles ran which routes? Are missing tests visible? Do repeated measurements establish consistency, and what do they leave uncertain? The chart should expose these limitations instead of quietly replacing missing values with zero. Then check independence. Validate the instrument, vary realistic operating conditions and investigate whether a system can recognise the standard test. If the gap persists, request an explanation that makes predictions which independent tests can challenge. Finally, separate causation from the anomaly. Exhaust measurements can show a serious discrepancy. Software evidence, documented decisions and admissions answer the question of deliberate manipulation. The conclusion is simple: independent road measurement made the hidden discrepancy visible. It justified further investigation. The later evidence established intent. Keeping those steps distinct gives us a stronger argument, and a more trustworthy way to evaluate the next impressive test result. SOURCE (not spoken): Analytical recommendations based on WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, pp. iv, 55, 57, 59, 64–65, and United States v. Volkswagen AG, Plea Agreement, 11 January 2017, Exhibit 2 (Statement of Facts), Exh. 2 ¶¶ 33–35, 54–55, 63. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 13
Likely audience questions
Did the road tests prove cheating?
They established the anomaly. Later software evidence and admissions established intent.
Why three vehicles?
Enough to identify cases worth investigating, insufficient to estimate fleet-wide prevalence.
Why use the standard on a road chart?
It provides a clear reference. The routes are not certification tests, and ratios must name their denominator.
Why do sources say 35×, ~40× or 10–40×?
Different scopes: route means (WVU), single runs (plea ¶ 52), drive cycles across the fleet (EPA p. 4).
WVU/ICCT (2014), p. iv, pp. 59, 64–65; EPA NOV (2015), pp. 3–4; VW plea (2017), Exh. 2, ¶ 34 (Exh. 2 p. 13), ¶ 52 (p. 21), ¶ 63.
13
Notes: Optional appendix; outside speaking time. Optional Q&A, outside the planned 15-minute talk. Did the road tests prove cheating? No. They revealed an anomaly. The later regulatory investigation and admitted facts established the software mechanism and deliberate concealment. Can three vehicles tell us about all diesels? No. The report explicitly limits its conclusions to the tested vehicles. Repeated routes improve understanding of those cases, not population coverage. Why compare road emissions with a laboratory standard? It is a useful reference for scale, provided we state what it is. Each road route is not itself a certification test. A multiple of the standard is different from a direct road-to-laboratory ratio. Why do the multiples differ between sources? Our chart shows route means, with a maximum of 35 times the standard. The plea agreement says the study vehicles reached up to about 40 times; A’s single San Diego run of 1.72 grams per kilometre is 40 times 0.043. The plea also says “sometimes 35 times” for the software generally, and the EPA notice says 10 to 40 times depending on the drive cycle. None of these is wrong; each has a different scope. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, p. iv, pp. 59, 64–65; EPA, Notice of Violation CAA-09-18-15, 18 September 2015, pp. 3–4; United States v. Volkswagen AG, Plea Agreement, 11 January 2017, Exhibit 2 (Statement of Facts), ¶ 34 (Exh. 2 p. 13), ¶ 52 (p. 21), ¶ 63. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 14
Primary sources
2014 research
WVU / ICCT report
15 May 2014
Design: pp. 1, 9–10, 50, 55, 57
Standard: Table 4.1 p. 59
Results: p. 64; Table 4.3 p. 65
2015 regulator findings
EPA Notice of Violation
18 September 2015
Switch and calibrations: pp. 3–4
Affected models: p. 5
2017 admissions
Volkswagen plea agreement
11 January 2017, Exhibit 2
¶¶ 30, 33–36, 49–64, 72
Penalties: pp. 12–14
Complete source details and links are also in the accompanying claim register.
14
Notes: Optional appendix; outside speaking time. Reference appendix. These sources support different stages of the argument: measured anomaly, regulatory findings, and admitted conduct. WVU page numbers are the report’s printed page numbers (PDF viewer page = printed page + 16 from Chapter 1 on). Plea Exhibit 2 page 2-N is PDF page N + 42. Full URLs and the claim-to-source table are in sources_and_claims.md. SOURCE (not spoken): Complete source details and links are also in the accompanying claim register. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=