## Slide 1
What was measured?
Laboratory
Controlled driving cycle
A and B: FTP-75 tests at CARB
Same prescribed speed sequence
Real roads
Portable exhaust measurement
Three vehicles, selected California routes
Traffic, hills and engine load vary
NOx = nitrogen oxides g/km = grams per kilometre
U.S. Tier 2 Bin 5 NOx standard: 0.043 g/km at full useful life
WVU/ICCT (2014), pp. 1, 9–10; Table 3.15 p. 57; Table 4.1 p. 59; p. 64. Standard = 0.07 g/mi (Table 2.2 p. 5).
1
Notes: Planned time: 75 seconds. Building on the claim we have just heard, my section asks how independent measurements tested it. In 2014, West Virginia University carried out an emissions study commissioned by the International Council on Clean Transportation. The researchers measured nitrogen oxides, or NOx, a group of air pollutants, in grams per kilometre travelled. In the laboratory, a chassis dynamometer, a set of rollers, lets a stationary car follow a prescribed driving cycle. Here that cycle is FTP-75, the standard U.S. laboratory sequence. The study tested Vehicles A and B on it. On the road, the researchers used a portable emissions measurement system, or PEMS: equipment carried by the car to measure its exhaust while it moves. Three vehicles drove selected routes, although not every vehicle ran every route. The benchmark is the Tier 2 Bin 5 NOx standard: 0.043 grams per kilometre at full useful life. It is a certification standard used as a reference; a road route is not itself the legal test. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, pp. 1, 9–10; Table 3.15 p. 57; Table 4.1 p. 59; p. 64. Standard = 0.07 g/mi (Table 2.2 p. 5). WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 2
What did the data show?
Chart: Mean NOx (g/km)
| Study lab FTP-75 | R1 Highway | R2 Los Angeles | R3 Rural hills | R4 San Diego | R5 San Francisco
Vehicle A (lean-NOx trap) | 0.022 | 0.614 | 0.989 | 1.505 | 1.48
Vehicle B (urea-SCR) | 0.016 | 0.344 | 0.809 | 0.671 | 0.675 | 0.815
Vehicle C (urea-SCR) | 0.048 | 0.07 | 0.409 | 0.053
Tier 2 Bin 5 standard, 0.043 g/km | 0.043 | 0.043 | 0.043 | 0.043 | 0.043 | 0.043
Bars: route or test means; thin bars: ±1 SD as published (none for single runs). No bar = no test (C lab, C R4, A R5), not zero.
The standard is a certification benchmark, used here as a reference; road routes are not certification tests. Three vehicles: no fleet-wide estimate.
WVU/ICCT (2014), Table 4.3 p. 65; laboratory results p. 64; standard Table 4.1 p. 59. Vehicle identities: EPA NOV (2015), p. 4.
2
Notes: Planned time: 95 seconds. Now look at the chart. Blue is Vehicle A, orange is B, and green is C. These are the report’s anonymous labels; the EPA later identified the two high emitters as a 2012 Jetta and a 2013 Passat, without saying which letter is which. The vertical scale is NOx in grams per kilometre. The dashed red line marks the standard. At the left, the study’s laboratory averages are 0.022 for A and 0.016 for B, both below that reference. Vehicle C has no laboratory result here. On the road, A reaches 1.505 grams per kilometre on the rural hill route. Dividing that by 0.043 gives 35 times the standard. The report summarises A as about 15 to 35 times the standard and B as about 5 to 20 times, depending on the route. Those ranges compare road emissions with the standard. They are not road-to-laboratory ratios or single observations. The green vehicle also matters. Its rural-route average is 0.409, roughly 9.5 times the standard, while its other route means are much lower. It provides useful context, but the vehicles differ, so it is not a controlled experiment. Error bars show the reported standard deviations, meaning variation around the average. Gaps mean no test result, not zero emissions. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, Table 4.3 p. 65; laboratory results p. 64; standard Table 4.1 p. 59. Vehicle identities: EPA, Notice of Violation CAA-09-18-15, 18 September 2015, p. 4. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 3
What did the discrepancy mean?
2014
Anomaly
Independent road measurements justified further investigation
2015
Mechanism
EPA described test detection and reduced control on the road
2017
Admitted conduct
Volkswagen admitted facts about design and concealment
The road data showed the gap. It did not, by itself, prove intent.
WVU/ICCT (2014), p. iv, pp. 62–64; EPA NOV (2015), pp. 3–4; VW plea (2017), Exh. 2 pp. 12–14, 21–24, ¶¶ 33–36, 54–55, 63.
3
Notes: Planned time: 65 seconds. The road data justified investigation because the gap was large and appeared across several routes. But road data alone did not prove intent, identify software, or show how common the behaviour was. That evidence came later. The EPA’s 2015 notice described a “switch”: software that read steering-wheel position, speed, engine run time and barometric pressure to recognise the official test, ran a compliant calibration in the lab, and weakened emissions control on the road. In its 2017 plea agreement, Volkswagen admitted designing that software and concealing it from regulators. So the research exposed an anomaly, and later evidence established deliberate manipulation. The line was not crossed in 2014, when the data looked bad. It was crossed years earlier, when the car was engineered to recognise the test. That is where the investigation picks up. SOURCE (not spoken): WVU/ICCT, In-Use Emissions Testing of Light-Duty Diesel Vehicles in the U.S., 15 May 2014, p. iv, pp. 62–64; EPA, Notice of Violation CAA-09-18-15, 18 September 2015, pp. 3–4; United States v. Volkswagen AG, Plea Agreement, 11 January 2017, Exhibit 2 (Statement of Facts), Exh. 2 pp. 12–14, 21–24, ¶¶ 33–36, 54–55, 63. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=

## Slide 4
Primary sources
2014 research
WVU / ICCT report
15 May 2014
Study design: pp. 1, 9–10, 57
Standard: Table 4.1 p. 59
Results: p. 64; Table 4.3 p. 65
2015 regulator findings
EPA Notice of Violation
18 September 2015
Switch and calibrations: pp. 3–4
WVU vehicles identified: p. 4
2017 admissions
Volkswagen plea agreement
11 January 2017, Exhibit 2
¶¶ 30, 33–36, 50–55, 58, 62–64, 72
Penalties: p. 13
Complete source details and links are also in the accompanying claim register.
4
Notes: Optional appendix; outside speaking time. Reference appendix. These sources support different stages of the argument: measured anomaly, regulatory findings, and admitted conduct. WVU page numbers are the report’s printed page numbers (PDF viewer page = printed page + 16 from Chapter 1 on). Plea Exhibit 2 page 2-N is PDF page N + 42. Full URLs and the claim-to-source table are in sources_and_claims.md. SOURCE (not spoken): Complete source details and links are also in the accompanying claim register. WVU: https://theicct.org/wp-content/uploads/2021/06/WVU_LDDV_in-use_ICCT_Report_Final_may2014.pdf EPA: https://www.epa.gov/sites/default/files/2015-10/documents/vw-nov-caa-09-18-15.pdf DOJ: https://www.justice.gov/archives/opa/press-release/file/924436/dl?inline=